## Slide 1: Hardware Design of Real-time Classification Algorithm Project Proposal
Haining Qiu, Harry Zhao, Justin Qiao, Qikun Liu

## Slide 2: Specification
The purpose of this project is to recognize a handwritten character image using the TRDM-D5M camera mounted on the DE1 FPGA board. The captured image will be processed by the hardware, namely the extended 552 processor with our assembly code.
The weight of the softmax linear classification is obtained using python pre-training algorithm and is preloaded into the ROM on the FPGA.
By using floating point matrix multiplication to process the image, we will obtain the predicted image category with high precision.
Finally, we will display the predicted image through UART to a host machine. An alternative would be displaying the classified result through VGA.

## Slide 3: IEEE 754 Floating Point Format
s
eeee_eeee
mmm__mmmm_mmmm_mmmm_mmmm_mmmm
value = (-1)^S * 2^(E-127) * (1.M)
when |E = 0, value = (-1)^S * 2^(E-127) * (0.M)
+0 = 32'h0000_0000, -0 = 32'h8000_0000
+INF = 32'h7F80_0000, -INF = 32'hFF80_0000
0x00000001 = 2^−126 × 2^−23 = 2^−149 ≈ 1.4012984643 × 10^−45 (smallest positive subnormal number)
0x007fffff = 2^−126 × (1 − 2^−23) ≈ 1.1754942107 ×10^−38 (largest subnormal number)
0x00800000 = 2^−126 ≈ 1.1754943508 × 10^−38 (smallest positive normal number)
0x7f7fffff = 2^127 × (2 − 2^−23) ≈ 3.4028234664 × 10^38 (largest normal number)

## Slide 4
Image_recognition.sv
CameraIN
Extended CPU
BMP_display
rst_synch
SW[9:0]
LEDR[9:0]
clk
decode
Spart
tx
key0
clk
rst_n
Monitor
Preloaded_weight_ROM
rx

## Slide 5: Floating Point Adder (IEEE format)
S1
S2
E1
E2
M1
M2
Subtraction and comparator
Shift M with smaller E to right by diff bit
normalize
out
FP_add.sv
Larger E
25-bit adder
diff
2’s comp
conversion

## Slide 6: Floating Point Multiplier (IEEE format)
S1
S2
E1
E2
M1
M2
1-bit XOR
8-bit adder
24 by 24 unsigned mul
Append 1 to the left
normalize
out
FP_mul.sv

## Slide 7: Note about multiplication
We will share a 25 by 25 (appending sign bit accordingly) multiply multiplier with just a * sign for IEEE FP multiplication, 16 by 16 signed multiplication and 16 by 16 unsigned multiplication in the beginning. This entails we will have a special module called multipliers sitting aside as the ALU to handle these three operations.
If this logic do not fit on the FPGA, we will proceed with the multi-cycle multiply as drawn in the next slide, this entails we won’t follow the standard IEEE floating point definition.

## Slide 8: Our Customized Floating Point Arithmetic (backup plan)
s
eeee_eeee_eeee_eeee
mmm_mmmm_mmmm_mmmm
Value = [(-1)^S] * (2^E) * (1.m), this 1 on the left of the decimal point is restricted to be 1
E is 16-bit signed, m is 15-bit unsigned (let M be 1.m), value sign depend on S
There is NO representation of absolute 0, but a number can be as small as ± 2-2^15, which is very close to 0. After an addition, we also need to check for 0. If a 0 occurs, we need to set the number to 2-2^15, which is 0x40000000 in this format. When dealing with negative numbers, we need to append the strict 1 in front of M, as “1.{M}”, then insert a 0 in front to indict the unsigness, as “01.{M}”. If the signed bit is set, then we convert the “01.{M}” into 2’s complement, then perform add. If the result is negative, then we convert it back to unsigned form and set its negative bit.
If any of the operands equals to 0x40000000, the result of multiplication is also 0x40000000, and the result of addition is the value of the other operand.
normalize(S, E, M) function - using shifters to ensure S, E, M follow FP definition
FP Addition V1 + V2: 1. Shift the smaller number to the right until the exponents of both numbers are the same. Increment the exponent of the smaller number after each shift. E’ represents the common E (the larger one)
2. Add M of each number as an integer calculation, M’ is the result of this step
3. S’ is determined by the number with larger abs
4. Vout = normalize(S’, E’, M’)
FP Multiplication V1 * V2: S’ = S1 ^ S2, E’ = E1 + E2, M’ = M1[15:0] * M2[15:0] Vout = normalize(S’, E’, M’)

## Slide 9: 16-by-16 Four-cycle Multiplier (backup plan)
16x4 single-cycle signed multiplier
Accumulator
Left shifter by 4
32-bit adder
mul0
mul1
SM control
(counter)
out
16x16_multiplier.sv
rdy
start
Mux
0
Notes: [3:0] [7:4] [11:8] [15:12]

## Slide 10: Floating Point Adder (backup plan)
S1
S2
E1
E2
M1
M2
Subtraction and comparator
Shift M with smaller E to right by diff bit
normalize
out
FP_add.sv
Larger E
17-bit adder
diff
2’s comp
conversion

## Slide 11: Floating Point Multiplier (backup plan)
S1
S2
E1
E2
M1
M2
1-bit XOR
16-bit signed adder
16x16_multiplier.sv
Append 1 to the left
Unsigned
normalize
out
FP_mul.sv

## Slide 12
CPU.sv
Fetch
Decode
Execute
Data
Mem
Write
Back
IF
ID
IDEX
EX
MEM
MEM
WB
Floating Operations
Multipliers

## Slide 13: ISA
We expand the provided 552 ISA to a 32-bit one while maintaining the original 16-bit structure. All original instructions preserve their opcodes with an extra bit 0 added in MSB. All new instructions start with bit 1 for clear differentiation. The register file is also expanded to 32 registers with 5-bit selecting address. This expansion enables functions including floating-point operations, integer multiplication, stack management, and instruction read.
https://docs.google.com/spreadsheets/d/1PT7VjIhUPUwOg7ZNtqeGGRNTjavUGF0D/edit?usp=sharing&ouid=115717939913064443857&rtpof=true&sd=true
The next page also has a screenshot of the ISA

## Slide 15: Possible Improvements
Specialized operation for the matrix multiplication on FPGA - we are considering the possibility of loading multiple data of the matrix and perform multiple multiplications simultaneously. (Tiny expansion of superscalar, VLIW, multi-cycle calculation)
Superscalar processor to perform the calculation of matrix multiplication (without Out-Of-Order schedule algorithm). This project would have little dependency in assembly code, so a superscalar processor could still perform well without OOO processing.
Out-Of-Order execution. This is the ultimate form of the project (unlikely to be accomplished). This will increase the performance of the classifier.

## Slide 16: Division of Labor
High-level Image Classification Algorithm Training | Qikun Liu | Out of order processing - add reorder buffer | Haining & Justin
Camera Interface and Demo Assembly Code | Qikun Liu & Haining Qiu | Out of order processing - add scheduler | Harry Zhao
Integrate classifier weights into top level | Qikun Liu | Out of order processing - verification | Everyone
Assembler for New ISA | Harry Zhao | Super Scalar Top level plan | Harry Zhao
Floating-Point Adder (and subtractor) | Haining Qiu | Super scalar - stall logic | Haining Qiu
Floating-Point (and integer) Multipliers | Justin Qiao | Super scalar - Compute unit integration | Justin Qiao
Int-FP and FP-Int Converters | Justin Qiao | Super scalar - wide fetch, wide decode | Harry Zhao
Processor Expansions for 32-bit ISA | Harry Zhao | Super scalar - memory modification | Qikun Liu
Unit Tests and Top-level Testbench Design | Everyone | Synthesis - Memory Management and Timing | Harry Zhao
Compiler to translate a classifier into asm code | Qikun Liu | Test Coverage | Justin Qiao

## Slide 17
05
W1
W2
W3
W4
04
W1
W2
W3
W4
03
W1
W2
W3
W4
Lorem ipsum
Lorem ipsum
Lorem ipsum
Lorem ipsum

## Slide 18
Extended ALU
src1
func
src0